## Slide 1: Geothermal heat extraction from abandoned mines
M
Jeroen van Hunen, Julien Mouli Castillo, Michael MacKenzie, Alexandra Sweeney, Charlotte Adams & GEMS team
Painting of Murton Colliery in 1843 by John Wilson Carmichael
In this talk:
Introduction to mine water heating
Modelling mine water heating
Application: mine water heating in Durham
Challenges and limitations
IAS and IDAS event on modelling, 2nd May, 2023

## Slide 2
Geothermal potential of mines
World’s total energy consumption in 2020: ~17 TW
Heat released into space 44 TW (or 60 mW/m2)
Thermal gradient ~ 20-30o / km
Marechal & Jaupart, 2011
Farr et al., 2020
Mine temperatures
Global surface heat flow

## Slide 3: Mine water geothermal heating (MWGH)
>100,000 disused mines in Europe (UNECE), mostly flooded
~1 in 4 UK homes built on top of mines
Mine water temperature:
12-25oC
Heat pump technology can increase this to 40-50oC.
Coal mine in British Midlands
(Getty images)

## Slide 4
Image: Monaghan et al., 2021, https://doi.org/10.1144/qjegh2021-033

## Slide 5: Mine water heating schemes in Europe
Norway: Folldal Cu-Zn-S mine; Kongsberg silver mine
Spain: Barredo-Figaredo coal mines, Asturia
Germany: Alsdorf, North Rhine Westphalia, many in Saxony
Poland: Szombierki Colliery, Bytom
Czechia: Jeremenko coal mine, Svornost Ag-Co-As-U mine
UK: Gateshead coal mines
France: Lorraine coal mines
Netherlands: Oranje Nassau coal collieries, Heerlen
Dawdon colliery pumping station, county Durham, UK

## Slide 6: Optimizing mine water geothermal heat extraction
Re-injection of mine water essential
This risks ‘thermal breakthrough’
Modelling can provide quick and low-cost assessment
Main questions to answer:
  Which mines are suitable for MWGH?
  What are potential critical failure points?
  What is the long-term capacity for heat extraction and storage?
Potential users:
  Academics
  Geo-engineering companies
  Coal Authority
Monaghan et al., 2021

## Slide 7: Mining and Modelling Methods
Re-injection
Pillar&Room and Longwall mining
resulted in
galleries and ‘goaf’
modelled with fluid flow and heat exchange in:
pipe network and FEM porous medium
Typical mine plan: Hutton coal seam below Durham
GOAF
ROOM & PILLAR

## Slide 8: Workflow
1) Digitising mine plans
2) Flow though mine workings
3) Calculate heat exchange
between water and
rocks
water
NODE i
NODE j
PIPE j
Hi
Hj
Qij
r0
r
water
rock
NODE i
NODE i+1
PIPE j

## Slide 9: Simple example: two-gallery system
re-injection
point
abstraction
point

## Slide 10: Case study: Mine water heating at Durham University
Feasibility study for several premises at the University site.
Utilizing the Hutton (upper) and Busty (lower) seams
Flow rate 6.5 litres/sec  191 kW of heat  heat for one building
Water inflow T: 8.5oC
Rock T: 11oC (Hutton) & 13.5oC (Busty)
Planned operation time: ~30 years

## Slide 11: Hutton and Busty coal seams
Hutton seam:
1858-1908
62 m deep,
1.1 m thick
~35,000 m3 extracted coal
Busty seam:
1870-1935
145 m deep,
1.3-1.8 m thick
~800,000 m3 extracted coal
(MacKenzie, 2022)

## Slide 12
~ 4 km
Hutton Seam 62 m bgl
Busty Seam 145 m bgl
~13.5 °C
~11 °C
Tout = 12.7 °C
Mouli-Castillo et al. in prep
Default scenario:
1 user, 6.4 litres/sec, 1 shaft
Tinflow = 8.5 °C
Tmax = 13.5 °C
Notes: 15 % Tout drop in 30 years

## Slide 13
~ 4 km
~13.5 °C
~11 °C
Tout = 10.7 °C
Mouli-Castillo et al. in prep
Effect of second, nearby shaft
Tinflow = 8.5 °C
Tmax = 13.5 °C
Notes: 15 % Tout drop in 30 years

## Slide 14
~ 4 km
~13.5 °C
~11 °C
Tout = 10.3 °C
Mouli-Castillo et al. in prep
Effect of larger flow rate: 6.4  64 litres/sec
Tinflow = 8.5 °C
Tmax = 13.5 °C
Notes: 15 % Tout drop in 30 years

## Slide 15
~ 4 km
~13.5 °C
~11 °C
Tout = 12.3 °C
Mouli-Castillo et al. in prep
Tout = 13.3 °C
Effect of second user
   
Tinflow = 8.5 °C
Tmax = 13.5 °C
Notes: 15 % Tout drop in 30 years

## Slide 16: Challenges and limitations
Uncertainty in state of mines:
  Backfilling of mines
  Pillar robbing and map chronology
  Mine abandonment
  Mine collapse
Availability of data to calibrate models
  MWGH relatively new
  Limited potential for measurements
  Successful projects provide limited data
Social/economical/regulatory challenges:
  Social acceptance and retro-fitting
  Investors and financial feasibility
  Ownership and licenses
Mine plans of
the Hutton seam

## Slide 17: Conclusions
MWGH is large sustainable energy source if responsibly used
Modelling can provide low-cost pre-drilling technical feasibility estimates
Durham case study illustrates critical components:
  Flow rates and pathway should allow enough time for water to re-heat
  State of mines uncertain; shaft conditions are critical
Challenges:
  Uncertainty in state of mine
  Availability of data to calibrate models
  Social/economical/regulatory challenges

## Slide 19: How does a heat pump work?
compressor
radiator
Coefficient of Performance (COP) ~4
(i.e. 1 kW electricity  ~4 kW heat)

## Slide 20: Flow calculation
water
NODE i
NODE j
PIPE j
Hi
Hj
Qij
r = resistance coefficient
n = flow exponent
qi = injection/abstraction at node i
Solve
A = matrix for equation (1)
F = net flow balance equation (2)
(1)
(2)
Update Q
Update A and F
Method by (Todini & Pilati, 1988)

## Slide 21: Heat transfer
r0
r
water
rock
NODE i
NODE i+1
PIPE j
Heat
conduction
Dittus-Boelter
advective heat transfer
Semi-analytical method
Energy balance: DEwater = -DErock
Heat transfer limited by:
Diffusive heat transfer in rock
Advective heat transfer in water
Method by (Rodrigues and Diaz, 2009)

## Slide 22: GEMS Research Project
Sept. 2021 – Aug. 2024, £1.7M EPSRC+NERC funding
Durham University:
  Earth Sciences: Jeroen van Hunen (PI), Julien Mouli-Castillo,
  Stefan Nielsen, Stuart Jones
  Engineering: Zhiwei Ma, Susmita Koley, Tony Roskilly, Huashan Bao
  Anthropology: Simone Abram, Chima Anyadike-Danes, Sandra Bell
  Business School: Laura Marsiliani, Jingyuan Di
  DEI / Heat Hub: Jacki Bell
British Geological Survey:
  Alison Monaghan, Anna Hicks, Johanna Scheidegger, Andres Gonzalez Quiros
Project partners:
  Mijnwater BV Heerlen
  Lanchester Wines
  Coal Authority
  GeoEnergy Durham
  Glacier Energy
  Clyde Gateway
  Durham County Council
  NEIMME
  Townrock Energy

## Slide 23: The end user
Disruption:
Gas boilers to be phased out
Lower temperature heat source and using our heat differently may require retro-fitting
Costs:
Capital costs (equipment + retrofitting)
Running costs (COP vs. electricity:gas price)
Environmental costs
 Work on solutions with end users
(MacKenzie, 2022)
3.9
4.5 (for 2021)
Notes: https://floorheating-direct.co.uk/
https://www.tricityappliance.com/blog/2018/october/the-pros-and-cons-of-a-gas-boiler/

## Slide 24: New regulations / policies / finance schemes
Recommendations on:
Regulations: Mine water geothermal heat is relatively new energy source in UK:
  Requirement for new government regulations?
  (e.g. Who owns heat underground?)
Financing: Risks associated with new mine water heating schemes and consequences for investors
Socio-economic impact: ensure a socially just energy transition
Images: Shutterstock; National business capital; Durham Record Office
Notes: http://www.durhamrecordoffice.org.uk/article/10597/Coal-Mining