## Slide 1: LHC upgrade: accelerator challenges
LHC machine status, and plans for HL-LHC
Mike Lamont
Acknowledgements: Lucio Rossi & Oliver Brüning

## Slide 2
LS1 - descent into the underworld again

## Slide 3
« Old Splice » « Machined Splice » « Consolidated Splice »
« Insulation box »
« Cables » « New Splice »
Total interconnects in the LHC:
  1,695 (10,170 high current splices)
Number of splices redone: ~3,000 (~30%)
Number of shunts applied: > 27,000
And a lot more besides…

## Slide 4: Superconducting Magnets and Circuits Consolidation (SMACC)
Collaborations with NTUA (Athens), WUT (Wroclaw) and support of DUBNA
Monumental effort
Over 350 persons involved
Including preparation: ~1,000,000 working hours
No serious accidents!
Jean-Philippe Tock

## Slide 5
Version 4.1
c/o Marzia Bernardini & Katy Foraz
9th March 2015
Today

## Slide 6: CSCM (Copper Stabilizer Continuity Measurement)
Connect the two 6 kA/200 V power converters in series
Stabilize the sector 20 K so the magnets and bus are not superconducting.
Apply a current of a few 100 A to open the bypass diodes
Apply a current pulse of 6.5 TeV equivalent and watch carefully
Fully qualify magnet bypass = copper stabilizer of the bus-bar + diode + diode leads
Bypass contains about 3500 connections/joints per sector!

## Slide 7: Signals from 11.1 kA run
Sector 67

## Slide 8: Cool-down - status
Sector 12 | 1.9 K | Prep. for powering tests | CSCM OK
Sector 23 | 20 K |  | CSCM OK
Sector 34 | 26 K | Cool-down | 
Sector 45 | 20 K | CSCM just starting | 
Sector 56 | 1.9 K |  | CSCM OK
Sector 67 | 1.9 K | First training quench… | CSCM OK
Sector 78 | 5 K |  | CSCM OK
Sector 81 | 1.9 K | Powering tests started | CSCM OK

## Slide 9: Powering tests
All magnet circuits taken to nominal current (6.5 TeV) one by one
  Rigorous checks of quench protection, energy extraction, interlocks, power converter…
800 lb gorilla is the main dipoles
  100 or so quenches expected to get to 6.5 TeV
  One so far in sector 67 at around 5.8 TeV
S67
1st training quench

## Slide 10: 2015 Q1/Q2
FIRST BEAM 9th MARCH
SCRUBBING FOR 50 ns
SCRUBBING FOR 25 ns
Official GPD luminosity target for the year: 10 fb-1

## Slide 12: Luminosity
N | Number of particles per bunch
kb | Number of bunches
f | Revolution frequency
σ* | Beam size at interaction point
F | Reduction factor due to crossing angle
ε | Emittance
εn | Normalized emittance
β* | Beta function at interaction point
Round beams, beam 1 = beam 2

## Slide 13
LHC bunch structure - 2015
1 SPS batch
(288 bunches)
26.7 km 2800 bunches
Abort gap
1 PS batch
(72 bunches)
25 ns bunch spacing
Nominal bunch intensity 1.15 x 1011 protons per bunch

## Slide 14: Squeeze in ATLAS
Image courtesy John Jowett
βmax ~20 km
β* = 15 cm
7 microns
2.6 mm
βmax ~4.5 km
β* = 55 cm
HL-LHC

## Slide 15: Crossing angle
work with a crossing angle to avoid parasitic collisions.
Separation: 10 -12 s

## Slide 16: Crossing angle
Large crossing angle:
 reduction of long range beam-beam interactions
 reduction of beam-beam tune spread and resonances
 reduction of the mechanical aperture
 reduction of luminous region
 reduction of overlap & instantaneous luminosity
geometric luminosity
reduction factor:

## Slide 17: HL-LHC - goals
Prepare machine for operation beyond 2025 and up to 2035
Devise beam parameters and operation scenarios for:
  total integrated luminosity of 3000 fb-1 in around 10-12 years
  an integrated luminosity of 250 fb-1 per year
  mu ≤ 140 (peak luminosity of 5x1034 cm-2s-1)

## Slide 18: How?
Beam from injectors
  High bunch population, low emittance, 25 ns beam
Lower beta* (~15 cm)
  New inner triplet magnets - wide aperture Nb3Sn
  Large aperture NbTi separator magnets
  Novel optics solutions
Crossing angle compensation
  Crab cavities
Dealing with the regime
  Collision debris, high radiation
  High machine availability
  Beam

## Slide 19: HL-LHC: key 25 ns parameters
Protons per bunch | 2.2 x 1011
Number of bunches | 2750
Normalized emittance | 2.5 micron
Beta* | 15 cm
Crossing angle | 590 microrad
Geometric reduction factor | 0.305
Virtual luminosity | 2.4 x 1035 cm-2s-1
Levelled luminosity | 5 x 1034 cm-2s-1
Levelled <pile-up> | 140

## Slide 20
1. Beams from injectors

## Slide 21: LIU proton target  HL-LHC beam parameters
25 ns | N (x 1011 p/b) | e (mm) | Bl (ns)
Achieved in 2012 | 1.2 | 2.6 (std) 1.4 (BCMS) | 1.5
HL-LHC | 2.3 | 2.1 | 1.7
Injectors must produce 25 ns proton beams with about double intensity and higher brightness
A cascade of improvements is needed across the whole injector chain to reach this target
Malika Meddahi

## Slide 22
BOOSTER: 160 MeV to 2.0 GeV
PS: 2 GeV to 26 GeV
LINAC4: H- at 160 MeV

## Slide 23: Main means to achieve the target HL-LHC proton beam parameters
Linac4 in for Linac2 | H- injection into PSB at 160 MeV Expected double brightness for LHC beams out of the PSB
Booster | Increase energy to 2 GeV New (or upgraded) RF system New main power supply
PS | Injection at 2 GeV Beam production schemes (e.g. BCMS) Feedback systems: new wide-band longitudinal feedback; transverse feedback against head-tail and e-cloud instabilities
SPS | Power upgrade of the main 200 MHz RF system (plus double available 800 MHz voltage) Electron cloud mitigation through a-C coating (baseline) or beam induced scrubbing
Many other options plus a full ion upgrade program
Malika Meddahi

## Slide 24: 2. LOWER beta*

## Slide 25: Triplets
Present LHC triplets: 210 T/m, 70 mm coil aperture
  8 T @ coil - approaching limit of NbTi
HL-LHC triplet: 140 T/m, 150 mm coil aperture
  Around 12 T @ coil
  Requires Nb3Sn technology
25 year development for this new magnet technology -
US-LARP/CERN collaboration
1.8K

## Slide 26: LHC low-β quads: steps in magnet technology from LHC toward HL-LHC
LHC (USA & JP, 5-6 m)
70 mm, Bpeak 8 T
1992-2005
LARP TQS & LQ (4m)
90 mm, Bpeak 11 T
2004-2010
LARP HQ
120 mm, Bpeak 12 T
2008-2014
LARP & CERN
MQXF
150 mm, Bpeak 12.1 T
2013-2020

## Slide 27: New interaction region layout
LHC
HL LHC
ATLAS
CMS
ATLAS
CMS
Superconducting separation dipoles (D1)
Corrector package
And beyond…
New triplets are not enough by themselves

## Slide 28: International magnet zoo
Triplet QXF (LARP and CERN)
Separation dipole D1 (KEK)
Recombination dipole D2
(INFN design)
Q4 (CEA)
Skew corrector (INFN)
Corrector sextupole (INFN)
Corrector dodecapole (INFN)
Corrector octupole (INFN)
Corrector decapole (INFN)
Orbit corrector (CIEMAT)
Cross-sections in scale
Ezio Todesco

## Slide 29
Small b* is limited not only by aperture but : optics matching, chromatic effects...
A novel optics scheme was developed to reach un-precedent b* w/o chromatic limit based on a kind of generalized squeeze involving 50% of the ring
Beam sizes [mm] @ 7 TeV from IR8 to IR2 for typical ATS
“pre-squeezed” optics (left) and “telescopic” collision optics (right)
b*= 40 cm
b*= 10 cm
The new IR is sort of 8 km long !
(S. Fartoukh)
Low beta* optics (ATS)

## Slide 30: 3. Crossing angle compensation

## Slide 31: Crab cavity development
RF-Dipole Nb prototype [ODU-SLAC]
DQWR prototype (17-Jan-2013) [BNL]
Major R&D program
Now concentrate on two designs in order to be ready for test installation in SPS in 2016/2017 TS
RF Dipole: waveguide or
waveguide-coax couplers
Double ¼-wave: coaxial couplers with
hook-type antenna

## Slide 32: Excellent results: e.g. RF dipole > 5 MV
Quench
4.2 K result
2 K result
Initial goal was 3.5 MV however V > 5-6 MV would ease integration
5
JP Delahayen ODU

## Slide 33: Crab kissing
Usual configuration in the || plane
Kissing Configuration in the || plane
Crab-cavities in the separation plane
Aim: lengthen luminous region to reduce pile-up density

## Slide 34: 4. DEALING with the regime
Losses in Stable Beams 2012: 50 ns, 1370 bunches, 1.6e11 ppb

## Slide 35: DS collimation
Replace a 8.3 T Nb-Ti dipole with two 11 T Nb3Sn dipoles
  Leaving enough space for a 0.8 m long room temperature collimator
Ezio Todesco – Chamonix 14
Protecting the dispersion suppressors (DS) from collimation or luminosity debris
  4 units needed for IP2 in LS2 – first Nb3Sn seeing a beam!
  8 units needed for IP7 in LS3
  Up to 16 more units could be needed at IP5 and IP1 in LS3

## Slide 36: Prototyping of cryogenics bypass
Prototyping of the by-pass crystostat (QTC) for the installation of a warm collimator in the cold dispersion suppressors.
MBHSP02 passed 11 T during training at 1.9 K with I = 12080A on 5th March 2013!

## Slide 37: The critical zones around IP1 and IP5
More than 1.2 km of LHC
Plus technical infrastructure
(e.g. Cryo and Powering)…
ATLAS
New triplet Nb3Sn
required due to:
-Radiation damage
-Need for more aperture
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11T Nb3Sn dipole
CMS

## Slide 38
Equipment on the Beam | Tunnel equipment | Vert. J | Surface Eq. | Dis.
DF(X-M) +
SC Link DSH (X-M)
Cryo line
Alignment
QPS2
Magnet system
MQXFA MQXFB, MBXF, MBRD, MQYY,
Q5 1.9, Q6 1.9
MCBXFB, MCBXFA, MQSXF, MCTXF, MCTSXF, MCDXF, MCDSXF, MCOXF, MCOSXF, MCSXF,MCSSXF,
MCBRD, MCBYY
Beam vacuum
TAXS, TAXN
Interaction Region and MS
IP 1,5
Collimation (TCTPM, TCL, TCLM, TCTP)
Beam diagnostic
BPMSQW, BMPSQ, BPMSQT, BMLC
DS Collimation for ion
IP 2
H.F. dipoles
Cryo-bypass+TCLD
DFH(X-M) +
Power converters
EE
Crab Cavity cryomodules
RF system
Loads, circulators, RF power, LLRF, HVPS, central LLRR
DS Collimation pp (TBC RUN II)
IP 1,5
H.F. dipoles
Cryo-bypass+TCLD
DS Collimation pp (TBC RUN II)
IP 7
H.F. dipoles
Cryo-bypass+TCLD
Rad-hard electronics for
BLM and BPM
CC diagnostic and protection
P
I
C
BIS
DFA+
SC Link DSHA
DFHA +
Power converters
SC link/
Powering
arc
IP 1,5
Cryoplant
IP 1,5
CB
Warm compressor and other surface eq.
SC link/powering
IP 7
Hor. SC L. DSH + DFA
Power converters
New DSLM for Q6
Paolo Fessia

## Slide 39: A few other challenges
Beam stability
  New low impedance collimators
Beam lifetime & loss spikes
  Magnet quenches
Machine protection
  Failure scenarios - local beam impact - equipment damage
  Quench protection
Machine availability
  Radiation to electronics (SEUs etc.)…
Very bright beams, very high bunch population, very high beam current

## Slide 40: Powering cold circuits
L = 20 m
(252) 1 kA @ 25 K, LHC Link P7
To avoid radiation to electronics and personnel – move power converters, possibly to surface. High Temperature Superconducting (HTS) links.

## Slide 41: 2010 - 2035
LS3: HL-LHC upgrade – machine and experiments

## Slide 42: Conclusions
2015 should be interesting
HL-LHC well established - as is LIU
Good progress on main technological challenges
It will be challenging:
  Ambitious targets
  Big beams, low tolerance to losses, very good operational efficiency required
  Run 2 and 3 are going to provide a lot of useful input

## Slide 43: HL-LHC Baseline Summary:
Cryogenic system upgrade (IR1&5 and IR4)
Tungsten shielding for triplet
New large aperture triplet magnets (Nb3Sn)
New Large aperture Insertion magnets (NbTi)
Crab Cavities for compensation of geom. Reduction
Operation with Luminosity leveling
Collimation upgrade (DS and impedance)
R2E and superconducting link

## Slide 44: HL-LHC Options:
Hollow electron lens (halo beam removal)
Long Range Beam-Beam wire compensators (reduction of crossing angle)
Flat beam operation (reduction of crossing angle)
Crab Kissing Scheme
Higher or lower harmonic RF system (bunch profile and beam stability)

## Slide 45: 10 year plan
Run 3: 14 TeV c.m. with peak luminosity of ~2x1034 cm-2 s-1
Run 2: 13 to 14 TeV c.m. with peak luminosity of ~1.7x1034 cm-2 s-1
LS2: 18 months
Connection of LINAC4
LHC Injectors Upgrade
EYETS ~5 months
Extended year end technical stop (CMS)
LS3: 30 months
High Luminosity LHC