## Slide 1: Particle Identification European Strategy Update meeting - Durham
Antonis Papanestis
RAL – STFC

## Slide 2: Outline
Particle ID techniques:
  Time of flight
  Cherenkov radiation
    RICH detectors
    DIRC detectors
  Transition radiation
  dE/dx

## Slide 3: Trends
Higher energy colliders, higher luminosity
  More tracks in the detectors, higher momentum tracks
Babar particle ID
LHCb particle ID

## Slide 4: Increased hit multiplicity
Babar DIRC
LHCb RICH 1/2
Before time window
After time window
About 1000 hits per box

## Slide 5: Time of flight
Better time resolution, better particle ID
  Faster detectors
  Desired for all detector technologies
    As an extra dimension to reduce complexity
Expected PID performance for various path lengths and time resolutions

## Slide 6: TOF: ALICE experiment
Resistive plates made of glass.
2 X5 gaps : 250 mm
Readout by HPTDC chip (High Performance Time to Digital Converter)
s=50.8ps
3σ π/K separation up to 2.2 GeV/c and K/p separation up to 4 GeV/c.
http://aliceinfo.cern.ch/Public/en/Chapter2/Chap2_TOF.html

## Slide 7: TORCH
The focusing unit converts angles to positions allowing the measurement of propagation time
Multiple photons from the same track can improve the time accuracy

## Slide 8: RICH detectors
Performance parameters:
  Cherenkov angle resolution
  Number of photons
  Complexity of the event
    Detector occupancy
Increasing the number of photons:
  Improved mirror reflectivity
  Better detector geometrical coverage
  Improved detector Quantum efficiency

## Slide 9: Cherenkov angle resolution
Chromatic error
  For a given radiator the refractive index depends on the photon wavelength
  Work in the area where the refractive index is flat: optical
  Loss of photons
  Detectors with high QE in the optical
Aberrations from the optical system
  Move mirrors to desired positions for smallest possible “emission point error”
  If inside the detector acceptance, low material budget (composite) mirrors are needed
Detection point error
  Smaller pixel
    Helps with occupancy
    More channels
Improve tracking and add timing

## Slide 10: Photon detectors
Multi-Anode PMTs
  To be installed in the LHCb RICH Upgrade
  Much improved since 2005
MCPs (Micro Channel Plate detectors)
  LAPPD Large Area Picosecond Photon Detectors
SiPMs (Silicon Photo Multipliers)
  Arrays of Avalanche Photo-Dodes
HPDs (Hybrid Photon Detectors)
  Currently in use by LHCb RICH

## Slide 11: Ideal photon detector
Pixel size 1mm2
  SiPM, MCP
Low dead area (tiles)
  ?? Possibly all
Radiation hard
  MaPMT
Insensitive to magnetic fields
  SiPM, MCP
Good QE at visible (~50%)
  SiPM
Durability
  SiPM, MaPMT
Low dark counts
  MCP, MaPMT
Fast
  MCP
  Possibly SiPM
Cheap 

## Slide 12: Timing
Timing can reduce event complexity by association of photons to tracks/vertices
Can be used as an extra dimension
Benefits start at ~100 ps
LHCb event with 9 primary vertices seen by the RICH detectors with 125 (left) and 25 (right) ps resolution
ns

## Slide 13: Summary
RICH and TOF techniques have proved very successful for particle ID
The LHCb RICH, and the RICH for the LHCb Upgrade show what is possible to do at the moment
New photon detectors will be needed in the next generation experiments (LHCb Upgrade II)
Can we find other applications to speed up their development?
  SiPMs promising, but currently suffer from radiation damage
  LAPPDs a viable alternative
Is timing below 100 ps possible?
Good quality, large area, cheap mirrors from composite materials could be a key factor in the new generation RICH detectors