ttH in FeynHiggs
Bill Murray
RAL, CCLRC
w.murray@rl.ac.uk
ATLAS UK Physics meeting
Durham
What is Feynhiggs
ATLAS sensitivity
Possible change?
MSSM scenarios

---
Investigate ttH in SUSY?
mSUGRA inspired model
Use FeynHiggs 2.4.1
  - Feynman-diagrammatic code, major 2-loops
  - Degrassi, Heinemeyer, Hollik, Slavich and Weiglein
It requires Higgs parameters:
  - mA, tanβ
  - Also At, μ, msusy, m2, m3: radiative corrections
mh, mH, branching ratios, coupling, cross-sections

---
What SUSY parameters?
Investigate benchmark parameter sets
  - No-mix,
  - mh-max,
  - gluo-phobic,
  - small alpha-eff
  - CPX
Warnings!
  - watch for 'funny' points; some instabilities
  - In CPX scenarios do not set CP phase to 90 degrees!

---
h and H of MSSM: no-mix
tth can be seen for some parameters
ttH for others
Always a thin gap!

---
CPX scenario
ATLAS finds this difficult for MH+=150, tan-beta=5
Can ttH do more?

---
SM tth Higgs: 30fb-1
tth cross-section times branching ratio
A cross-section of 500 for tth allows interesting study
Nb: Final mass is not a good variable. If we don't use it can we ADD event rates?
Janice Droghan

---
ttH mass spectrum
Incorrect jet pairs, energy resolution, etc. spread peak

---
no-mixing Higgs masses
Plots show masses of h, H and A in plane mA v tan-beta
Black masses, >140GeV, have few tth
Maximum mass 120GeV
Mtop=172.5

---
mh-max Higgs masses
Plots show masses of h, H and A in plane mA v tan-beta
Black masses, >140GeV, have few tth
Maximum mass 135GeV
Mtop=172.5

---
CPX Higgs masses
Plots show masses of h, H and A in plane mA v tan-beta
Yellow: no solution found by FeynHiggs
Black masses, >140GeV, have few tth

---
Low α-eff Higgs masses
Plots show masses of h, H and A in plane mA v tan-beta
Black masses, >140GeV, have few tth
Mtop=172.5

---
No-mix tth rates
h, H and A tth rates
Fourth plot is total
Green is 500fb: two sigma?
Green+ for all parameter space
Sigma tth for Mh<80 not calculated: yellow

---
mh-max tth rates
h, H and A tth rates
Fourth plot is total
Green is 500fb: two sigma?
Falls towards 1 sigma for this scenario:
Always some sensitivity
!

---
Gluo-phobic tth rates
h, H and A tth rates
Fourth plot is total
Green is 500fb: two sigma?
Two sigma or better: no holes

---
CPX tth rates
h, H and A tth rates
Fourth plot is total
Green is 500fb: two sigma?
Hole at 150,5 gone?
Need to look at mH<80GeV

---
CPV tth rates
Other CPV scenarios
CPX but phase of At, M3 independent
  - (0,0)
  - (0,90)
  - (90,0)
  - (90,90)
There is always a decent signal
(0,90)
(0,0)
(90,90)
(90,0)

---
Small α-eff tth rates
h, H and A tth rates
This scenario designed to have small bbh coupling.
ttH, tth, bbh and bbH conspire
SUSY always has an escape route

---
Couplings of SUSY Higgs
tan 2 %alpha = tan 2 %beta ( {M_A^2+M_Z^2}over{M_A^2 - M_Z^2} )
Tree
level

---
Summary
MSSM higgs very often appears in tth
At least one of the Higgses should be there
  - Only very unusual parameter choices suppress it
Difficult region in CPX can be addressed
  - Search to mh below 80 should be included
Of course, it is a difficult channel
Only two sigma for 30fb-1.
But very great range of MSSM gives signals

---
SM Rates for 10fb-1
Rates in major channels
  - from Pythia
No cuts, just branching ratios
l: e or μ
LEP

---
h and H of MSSM: MhMax
tth can be seen for some parameters
ttH for others
ATLAS Preliminary 300fb-1
ttH
tth